## Slide 1
TAPIT
Engineering Co., Ltd.
https://mculearning.com
0981001119
fb.com/tapitvn
contact@tapit.vn
https://tapit.vn
STM32 MCU Programming Hybrid Learning Course
STM32 Analog-to-Digital Converter (ADC) – Part1
Nơi học Vi điều khiển tốt nhất Việt Nam!

## Slide 2
ADC introduction (SAR type)
SAR ADC
STM32
DATA
Cortex
M4
Memory
DMA
ADC_IN
Analog to Digital Converter
Notes: Analog signal
Digital signal

## Slide 3
STM32F303RE ADC
Ref Datasheet: https://www.st.com/resource/en/datasheet/stm32f303re.pdf

## Slide 4
ADC CHANNEL
Each ADC has up to 19 multiplexed channels
Internal Channel
External Channel
ADC external channels mapping:
Ref User Manual: https://www.st.com/resource/en/reference_manual/dm00043574-stm32f303xb-c-d-e-stm32f303x6-8-stm32f328x8-stm32f358xc-stm32f398xe-advanced-arm-based-mcus-stmicroelectronics.pdf

## Slide 5
ADC channel inputs can be configured in single-ended or differential mode
ADC CHANNEL INPUT MODE
Single-ended mode
Differential mode
Ref Differential and Single-Ended ADC: https://ww1.microchip.com/downloads/en/DeviceDoc/Differential-and-Single-Ended-ADC-WhitePaper-DS00003197A.pdf
Ref STM32F30x ADC modes and application:
https://www.st.com/resource/en/application_note/dm00069390-stm32f30x-adc-modes-and-application-stmicroelectronics.pdf
A differential ADC measures the voltage difference between two inputs.
A single-ended ADC measures the voltage an analog voltage signal on a single wire referenced to this common ground.

## Slide 6
ADC RESOLUTION
12, 10, 8 or 6-bit configurable resolution
VREF- ≤ VIN ≤ VREF+
VIN = VREF- VIN = VREF+
NADC = 0 NADC = 2^12 -1
0 ≤ NADC ≤ 2^12 -1
NADC = (2^12 -1) x
VIN – VREF-
VREF+ – VREF-
VIN
=
NADC x VDD
4095
*16bit data register -> DataAlignment (right alignment)

## Slide 7
STM32F30x ADC modes
Independent modes
Regular conversion mode
Injected conversion mode
Dual modes
Dual injected simultaneous mode
Dual regular simultaneous mode
Dual interleaved mode
Dual alternate trigger mode
Ref STM32F30x ADC modes and application: https://www.st.com/resource/en/application_note/dm00069390-stm32f30x-adc-modes-and-application-stmicroelectronics.pdf

## Slide 8
STM32F30x ADC modes
Independent modes
Regular conversion mode
Multichannel/Single, continuous mode

## Slide 9
STM32F30x ADC modes
Independent modes
Regular conversion mode
Multichannel/single, single conversion mode

## Slide 10
ADC SAMPLING TIME
Ref User manual: https://www.st.com/resource/en/reference_manual/dm00043574-stm32f303xb-c-d-e-stm32f303x6-8-stm32f328x8-stm32f358xc-stm32f398xe-advanced-arm-based-mcus-stmicroelectronics.pdf

## Slide 11
ADC SAMPLING TIME

## Slide 12
Polling
  HAL_ADC_Start(ADC_HandleTypeDef* hadc)
  HAL_ADC_PollForConversion(ADC_HandleTypeDef* hadc, uint32_t Timeout) uint32_t HAL_ADC_GetValue(ADC_HandleTypeDef* hadc)
HAL_ADC_Stop(ADC_HandleTypeDef* hadc)
Interrupt generation at End of Conversion, End of Injected
HAL_ADC_Start_IT(ADC_HandleTypeDef* hadc)
HAL_ADC_Stop_IT(ADC_HandleTypeDef* hadc)
DMA request generation during regular channel conversion
  HAL_ADC_Start_DMA(ADC_HandleTypeDef* hadc, uint32_t* pData, uint32_t Length)
  HAL_ADC_Stop_DMA(ADC_HandleTypeDef* hadc)
Get ADC Value
void HAL_ADC_ConvCpltCallback(ADC_HandleTypeDef* hadc) {
….. HAL_ADC_GetValue…
}

## Slide 13
ADC Poll lab
How to setup ADC in poll in CubeMX and Generate Code
How to Generate Code in CubeMX and use HAL functions

## Slide 14
Use ADC in polling mode
HAL_ADC_Start(DAC_HandleTypeDef* hdac, uint32_t Channel) HAL_ADC_PollForConversion(ADC_HandleTypeDef* hadc, uint32_t Timeout)
HAL_ADC_GetValue(ADC_HandleTypeDef* hadc)

## Slide 15
Use ADC in polling mode
/* USER CODE BEGIN 3 */
/* Infinite loop */
while (1)
{
  HAL_ADC_Start(&hadc1); HAL_ADC_PollForConversion(&hadc1,10); value_adc=HAL_ADC_GetValue(&hadc1);
  HAL_Delay(1000);
}
/* USER CODE END 3 */
=>Debug
/* USER CODE BEGIN PV */
uint32_t value_adc;
/* USER CODE END PV */

## Slide 16
ADC Interrupt lab
How to setup ADC in interrupt in CubeMX and Generate Code
How to Generate Code in CubeMX and use HAL functions

## Slide 17
TAB>NVIC settings
Use ADC with interrupt

## Slide 18
For ADC start use function
• HAL_ADC_Start_IT(ADC_HandleTypeDef* hadc, uint32_t Channel)
• HAL_ADC_GetValue(ADC_HandleTypeDef* hadc)
ADC complete callback function
• HAL_ADC_ConvCpltCallback(ADC_HandleTypeDef* hadc)
Use ADC with interrupt

## Slide 19
/* USER CODE BEGIN PV */
  uint32_t value_adc;
/* USER CODE END PV *
/* USER CODE BEGIN 2 */
HAL_ADC_Start_IT(&hadc1);
/* USER CODE END 2 */
/* USER CODE BEGIN 4 */
void HAL_ADC_ConvCpltCallback(ADC_HandleTypeDef* hadc)
{
  value_adc=HAL_ADC_GetValue(&hadc1);
  HAL_ADC_Start_IT(&hadc1);
}
/* USER CODE END 4 */
=>Debug
Use ADC with interrupt

## Slide 20
Instructor
Eng. Nguyen Huynh Nhat Thuong Eng. Tran Thuy Ngoc Hang
TAPIT
Engineering Co., Ltd.
0981001119
fb.com/tapitvn
contact@tapit.vn
https://tapit.vn
Notes: Cảm ơn các bạn.